## Slide 1
SMART GRID SECURITY
2K Innovators
Early-Warning Intelligent Power
Infrastructure Monitoring System
Proactive cable theft detection — even during load shedding.
Notes: Introduce GridGuard AI: a dual-layer hybrid monitoring system designed to detect cable theft in real time — even during outages and load shedding. This is a major problem in South Africa and developing nations.

## Slide 2
THE PROBLEM
Cable Theft Is Crippling Infrastructure
Prolonged Outages
Communities & businesses crippled — sometimes for days after theft events.
Financial Loss
Millions lost by municipalities in replacement costs and lost revenue.
Safety Hazards
Exposed live wires cause fatal electrocutions and widespread grid fires.
Reactive Response
Theft discovered only after frustrated residents report outages hours later.
Current monitoring relies on public complaints — theft is discovered AFTER the outage, sometimes hours later.
Notes: South Africa alone loses hundreds of millions yearly to cable theft. The core issue is reactive detection — by the time someone reports it, the cables are gone.

## Slide 3
THE SOLUTION
Hybrid Smart-Grid Monitoring Network
A distributed monitoring network combination:
Industrial-grade cable monitoring power supply at transformer level
Quick response to electrical disruption
Notifies service provider and municapalities
Resident mobile app for real-time notifications
Transformer Node
GSM Commander CTM001 + CM2
Main Distribution Cable Line
Household A
(ESP32/LoRa)
Household B
(ESP32/LoRa)
☁ AI Cloud Dashboard
Notes: The system has two layers: a master transformer node running GSM Commander hardware, and low-cost ESP32 endpoints at household meter boxes. Together they provide full visibility from the source to the end user.

## Slide 4
HARDWARE
The Technology Powering Hybrid Smart-Grid
GSM Commander CTM001
Transformer Node
AC load monitoring
DC continuity pulse injection
Dual-SIM cellular comms
Battery-backed — works during outages
ESP32 Endpoint Node
Household Meter Box
Voltage availability sensing
Load pattern monitoring
LoRaWAN / NB-IoT mesh
Low-cost, scalable deployment
AI Cloud Platform
Analytics & Dashboard
Real-time theft classification
Predictive risk mapping
Outage hotspot visualization
Resident mobile app alerts
Notes: Hardware overview: CTM001 is an industrial-grade unit deployed at transformer sites. ESP32 nodes are cheap, sub-$10 devices in household meter boxes. The AI cloud ties it all together.

## Slide 5
VALUE PROPOSITION
Why Choose GridGuard AI?
< 15s
Detection Time
from cable cut to alert
24/7
Monitoring
even during load shedding
GPS
Fault Localization
narrows search to meters
Competitive Advantage
Detects theft during load shedding
Better response time for dispatched units
Better statical reports that can improve physical infrustucture maintenance in the long term
Notes: Key selling point: GridGuard AI is the only solution that remains active during load shedding via DC continuity pulse injection. This is the window thieves currently exploit.

## Slide 6
HOW IT WORKS
Detection in Under 15 Seconds
1
AC Power Drops
Load shedding or theft event begins. Grid goes offline.
2
DC Pulse Activated
CTM001 switches to battery & injects DC continuity pulse.
3
Cable Severed
Thief physically cuts the cable — continuity loop breaks.
4
Instant Alert
CM2 unit transmits emergency alert via cellular network.
5
AI Classifies Event
Cloud AI distinguishes theft from regular outage within seconds.
6
Team Dispatched
Municipal team gets GPS-pinpointed alert. Residence notified.
Notes: Walk through the detection flow. The key innovation is step 2 — DC pulse injection means the system doesn't go blind during load shedding, when 80% of cable theft occurs.

## Slide 7
COST ESTIMATION
Deployment & ROI Overview
Hardware Costs (per unit — approximate)
Component | Unit Cost (ZAR) | Notes
GSM Commander CTM001 + CM2 | R 8,000 – R 12,000 | Per transformer site
Backup Battery Pack | R 1,500 – R 2,500 | 12V sealed lead-acid
SIM / Cellular Data Plan | R 150 – R 300 /mo | Per transformer node
Cloud Platform (SaaS) | R 500 – R 2,000 /mo | Per municipality zone
Typical Pilot Zone
(50 Endpoints + 5 Nodes)
~R 35,000 – R 65,000 Setup
vs. R 500K+ replacement per theft incident
ROI Break-Even
Prevention of a single theft incident typically covers the full pilot deployment cost — making GridGuard AI self-funding from day one.
Notes: Key ROI message: one prevented theft pays for the entire pilot zone installation. Municipalities spend 500K to 2M on each major cable theft incident in replacement and labor. GridGuard AI pays for itself immediately.

## Slide 8
Thank you
Protecting infrastructure, improving performance
before communities feel the dark.
Notes: Close with confidence. GridGuard AI is ready for pilot deployment. The demo at the hackathon shows a physical wire cut triggering a live dashboard alert and SMS — within 15 seconds.